## Slide 1
ARM CPU Emulator
Component 1: Instruction Decoder & Disassembler
Software & Systems Development | CRN 11550 | Level 7
32-BIT
ARM

## Slide 2
What I Built
VIRTUAL RAM
A 1024-word memory array that stores 32-bit ARM machine code instructions loaded from a file or hardcoded for testing.
INSTRUCTION DECODER
Uses bitwise operations (&, >>) to extract fields from each 32-bit instruction — condition code, opcode, registers, operands.
DISASSEMBLER
Prints the human-readable Assembly mnemonic alongside the raw hex op-code for every instruction decoded.

## Slide 3
The Fetch → Decode → Execute Loop
1
FETCH
registers[15] holds the PC.
memory[PC >> 2] reads the next 32-bit instruction.
PC is immediately incremented by 4.
→
2
DECODE
decodeInstruction() checks bits 27:26.
00 → ALU 01 → LDR/STR
10 → Branch 11 → SWI
The right decoder extracts all fields.
→
3
EXECUTE
(Component 2)
Component 1: just PRINTS the mnemonic.
Component 2 will actually perform
the operation and update registers.

## Slide 4
How Bit Decoding Works — E3A00001
Step 1 — The raw 32-bit instruction in binary:
1110 0011 1010 0000 0000 0000 0000 0001
Cond
[31:28]
= 0xE
= AL
00
[27:26]
ALU type
I=1
[25]
Immediate
OpCode
[24:21]
= 13
= MOV
S=0
[20]
No flag
Rn=0
[19:16]
(ignored)
Rd=0
[15:12]
= r0
#1
[7:0]
Step 2 — C code extracts each field:
int condCode = inst >> 28; // → 14 = AL (always execute) int opcode = (inst >> 21) & 0xF; // → 13 = MOV int regDest = (inst >> 12) & 0xF; // → 0 = r0 int imm = inst & 0xFF; // → 1 = #1

## Slide 5
Live Program Output
$ ./emulator test_all.txt Loading file: test_all.txt Address Op-Code Assembly Mnemonic -------------------------------------------------- 00000000 : E3A00000 MOV r0, #0 00000004 : E3A00B02 MOV r0, #2048 00000008 : E0832004 ADD r2, r3, r4 0000000C : E0932004 ADDS r2, r3, r4 00000010 : E0454006 SUB r4, r5, r6 ... 00000074 : EA000002 B 16 00000078 : 1AFFFFFC BNE -8 0000007C : EBFFFFFB BL -12 00000080 : EF000001 SWI 1 [End of program]

## Slide 6
All Instruction Types Supported
Bits 27:26 | Type | Instructions Covered | Count
0 0 | Data Processing (ALU) | AND EOR SUB RSB ADD ADC SBC RSC TST TEQ CMP CMN ORR MOV BIC MVN | 16
0 1 | Data Transfer | LDR / STR with all addressing modes (pre/post index, write-back, byte/word) | 2+
1 0 + B25 | Branch | B (branch) and BL (branch with link) | 2
1 1 | Software Interrupt | SWI with 24-bit interrupt code | 1
Any | All 16 Condition Codes | EQ NE CS CC MI PL VS VC HI LS GE LT GT LE AL NV | 16

## Slide 7
Condition Codes — Every Instruction Has One
Bits [31:28] of every instruction. The CPU checks the Status Register before executing.
EQ
Z=1
Equal
NE
Z=0
Not Equal
CS
C=1
Carry Set
CC
C=0
Carry Clear
MI
N=1
Minus
PL
N=0
Plus
VS
V=1
Overflow
VC
V=0
No Overflow
HI
C=1 Z=0
Higher
LS
C=0/Z=1
Lower/Same
GE
N=V
Signed >=
LT
N≠V
Signed <
GT
Z=0 N=V
Signed >
LE
Z=1/N≠V
Signed <=
AL
Always
(most instrs)
NV
Never
(unused)

## Slide 8
Operand 2 — The Flexible Second Argument
I = 1 (Immediate)
Bits [7:0] = 8-bit immediate value Bits [11:8] = rotate amount (×2) Examples: MOV r0, #1 MOV r0, #2048 ADD r2, r3, #5 A constant number baked directly
into the instruction itself.
I = 0 (Register + Shift)
Bits [3:0] = source register number Bits [6:5] = shift type (LSL/LSR/ASR/ROR) Bits [11:7] = shift amount Examples: MOV r1, r0, LSR #1 MOV r1, r0, LSL #2 ADD r2, r3, r4, ROR #4 Value from a register, optionally
shifted before use.

## Slide 9
Key Questions — What to Expect in the Demo
Q: How does your program know it's a MOV?
A: Bits 27:26 = 00 → ALU. Bits 24:21 = 1101 = 13. alu_op_labels[13] = "MOV".
Q: Why does the PC increase by 4?
A: Every ARM instruction is exactly 32 bits = 4 bytes. PC counts bytes, so +4 per instruction.
Q: What does the I bit do?
A: Bit 25 = 1: Operand2 is an immediate constant (#5). Bit 25 = 0: Operand2 is a register.
Q: Why use uint32_t not int?
A: int size varies by platform (16/32/64 bit). uint32_t is always exactly 32 bits — matches real ARM registers.
Q: What is the S bit?
A: Bit 20. If set (1), the instruction updates the Status Register flags. ADDS updates flags, ADD does not.

## Slide 10
What's Next — Component 2
Part A — Basic Emulation
Add actual execution — don't just print, DO the operation
Implement all ALU instructions: ADD, SUB, MOV, AND, ORR, CMP...
Display all 16 register values after each instruction
Step-by-step mode: pause and wait for Enter key
Track and update the Program Counter correctly
Part B — Full Emulation
Add conditional execution using Status Register flags
Implement LDR/STR to read and write virtual RAM
Implement B and BL to change the Program Counter
Set N, Z, C, V flags correctly after each ALU operation
Count and display CPU cycle usage per instruction

## Slide 11
Component 1 — Complete
ARM Instruction Decoder & Disassembler
✓ All 16 ALU instructions decoded correctly ✓ All 16 condition codes handled ✓ LDR / STR with all addressing modes ✓ B, BL, and SWI ✓ File loading (prog1.txt → prog5.txt) ✓ Fully commented, well-formatted C code